## Slide 1
DEVELOPMENT OF BUS LANES AND SEPARATE INDEPENDENT ROUTES IN PUBLIC TRANSPORT PROJECT
Centre for Urban Development Planning – CEP Ltd Zahumska 34, Belgrade
Public Transport Consult – PTC Ltd
Poenkareova 12/11, Belgrade
XI 2020.

## Slide 2
DEVELOPMENT OF BUS LANES AND SEPARATE INDEPENDENT ROUTES IN PUBLIC TRANSPORT PROJECT
CITY OF BELGRADE – CITY ADMINISTRATION CITY OF BELGRADE Secretariat for public transport
27. marta 43-45, Belgrade
Client:
Contractor:
Centre for Urban Development Planning - CEP Public Transport Consult - PTC
Zoran RUBINJONI, M. Scs. TE | Prof. Slaven M. TICA, PhD TE
Stefan KNEŽEVIĆ, M. Scs. TE | Aleksandra LAZIĆ, M. Scs. TE
Goran ZIMONJIĆ, M. Scs. TE | Associate Prof. Predrag ŽIVANOVIĆ, PhD TE
Prof. Ana TRPKOVIĆ, PhD TE | Associate Prof. Stanko BAJČETIĆ, PhD TE
Snežana DIMITRIJEVIĆ, M. Scs. TE | Prof. Branko MILOVANOVIĆ, PhD TE
Katarina PANDUROV, M. Scs. ME | Assistant Prof. Andrea NAĐ, M. Scs. TE
Nataša MUJEZINOVIĆ, M. Scs. AE | Senior Associate Slobodan GAVRILOVIĆ, M. Scs. TE
Project team:

## Slide 3
METHODOLOGY
GOALS
Creating conditions for the improvement of the operation and productivity of the public transport system and the level of quality of transport services
Reduction of traffic congestion on identified critical sections of the line network
An increase of the operational speed in the public passenger transport system
A reduction in air pollution and an increase in the ecological suitability of the public transport system
More rational use of propulsion energy and an increase in the economic, energy and cost efficiency of the public transport system
An increase in quality of the transport service with an increase in efficiency and productivity of the Belgrade public transport subsystems
An increase in the quality of service and attractiveness of the system as a whole
Reduced driver stress
Promotion of public transport system use
Traffic safety improvement

## Slide 4
TASKS
Analysis of the current state of the prioritization system
Analysis of congested corridors and sections of line routes in the network in the central area of the city
Analysis of characteristic experiences concerning the introduction of the prioritization system to the line network of the public transport system
Defining criteria for the introduction of basic prioritization systems on the line network (bus lanes and independent routes)
Defining proposed improvements to the existing basic prioritization systems in the line network
Simulation of proposed solutions and impact assessment within the existing Belgrade Transport Model
Analysis of the effects of proposed solutions
Defining the implementation dynamic in the actual system
METHODOLOGY

## Slide 5
ANALYSIS OF THE EXISTING CONDITION
ANALYSIS OF THE EXISTING CONDITION OF BUS LANES IN BELGRADE
27.03.2020, a tour of the existing bus lanes was organized
Photographing and recording all sections of bus lanes
Total length of recorded videos is 2 h and 45 min
The total length of the bus lanes is 48,8 km
  Tram, trolleybus and bus 0,2 km
  Trolleybus and bus 3,9 km
  Tram and bus 15,2 km
  Bus 29,5 km
Bus lines exist in 30 streets in Belgrade

## Slide 6
OPERATION MODE AND METOD OF MONITORING AND CONTROL
9 streets have a mode of operation from 07:00 to 09:00 and from 14:00 to 18:00, on other streets there all day mode of operation bus lanes
Traffic signs at the beginning of the bus lanes exist in most cases, which is not the case for the end
All taxi stands are marked with appropriate traffic signals
Static traffic camera control exists at 4 locations in the Belgrade
THE PUBLIC TRANSPORT FUNCTIONING ANALYSIS OF BUS LANES
Analyses were conducted through extensive research of up-to-date databases on the system operation in the preceding period (data bases from the vehicle management system), in a stable mode of operation and a representative period of time, for the month of December 2019.
All sections with existing bus lanes – for each direction separately
The number of stops, the number of lines and number of public transport vehicle in the peak period were analyzed
During the analysis, all lines passing through the observed section were included, regardless of whether they have a stop on the route located on the section
ANALYSIS OF THE EXISTING CONDITION

## Slide 7
CASE STUDIES REGARDING THE INTRODUCTION OF BUS LANES
EXAMPLES OF WORLD PRACTICE IN OGRANIZATION AND DESIGN OF BUS LANES
The analysed cities were Vienna, Zagreb, Barcelona, Amsterdam, London, Paris, Los Angeles, New York, San Francisco, Seoul and Sydney.
This chapter describes the different experiences concerning institutional organisations, bus lane design, bus lane utilization and compliance control for vehicles of the public passenger transport system
London
Seul

## Slide 8
MICRO ANALYSIS OF BOTTLENECKS
Direction to the central city zone
Direction from the central city zone
CASE STUDIES REGARDING THE INTRODUCTION OF BUS LANES

## Slide 9
ANALYSIS OF BOTTLENECKS, CONGESTED CORRIDORS AND SECTIONS
MICRO ANALYSIS OF BOTTLENECKS
The public transport functioning analysis of the bus lanes was made on the basic of data obtained from the BusPlus system, and from the report of stopping vehicles at stops, timetable and the updated Transport Model of Belgrade
Lengths of space between stops were obtained from timetable, while driving times were obtained on the basis of the time of exit of the vehicle from the zone of the previous stop and entry of the vehicle into the zone of the observed
Driving time has been increased by 6 seconds, due to the vehicle registration system with a stop diameter of 20 m
The analysis included the terminus located in the central city zone, so the correction of driving time was performed separately for each terminus
Based the length of spacing between stops and corrected driving times, the realized driving speed of all vehicles in the system were obtained

## Slide 10
CRITERIA FOR THE INTRODUCTION OF BUS LANES
The methodology consists of multiple phases and in accordance with that two groups of evaluation criteria are used: basic and additional criteria
BASIC CRITERIA
Vehicle frequency: greater then 20 vehicles/h
Transport speed: lower than 10 km/h
ADDITIONAL CRITERIA
Passenger flow: greater then 800 passengers/h
Time loss in intersections : service level at intersections higher than „C“
Volume capacity ratio: service level no lower than „D“

## Slide 11
METHODOLOGY FOR THE SELECTION OF SECTIONS WHERE THE INTRODUCTION OF PHYSICAL PRIORITIZATION FOR PUBLIC TRANSPORT
CRITERIA FOR THE INTRODUCTION OF BUS LANES

## Slide 12
STREETS AND SECTIONS WITH PROPOSED CHANGES AND INTERVENTIONS
No. | Street | Section | Proposed operation mode intervention
1. | Kralja Milana, Terazije, Kolarčeva | From Slavija to Trg Republike | Only open for public transport vehicles, cyclists, residents and pedestrians.
2. | Resavska | From Bulevar kralja Aleksandra to Nemanjina | Only open to public transport vehicles and residents.
3. | Dečanska | From Bulevar Despota Stefana to the Terazije tunnel | Bus lane for public transport vehicles in a newly constructed lane.
4. | Brankova | Brankov most stop | Extend the “Brankov most” stop in the direction towards New Belgrade and mark a pedestrian/cyclist path.
5. | Ruzveltova, Mije Kovačevića | From Omladinski stadion to Bulevar kralja Aleksandra | Bus lane for public transport vehicles (both directions).
6. | Bulevar kralja Aleksandra | From Kneza Miloša to Ruzveltova | Bus lane for public transport vehicles (both directions)
 |  | From Cvetkova pijaca to Ustanička | Bus lane for public transport vehicles (both directions)
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 13
STREETS AND SECTIONS WITH PROPOSED CHANGES AND INTERVENTIONS
No. | Street | Section | Proposed operation mode intervention
7. | Bulevar kralja Aleksandra | From Kneza Miloša to Ustanička | Light signals – tram prioritization
8. | Cara Dušana, Džordža Vašingtona, 27. marta, Kraljice Marije | Following completion of works – entire length | Bus lane for public transport vehicles (both directions).
9. | Dobračina | Entire lenth | Only open for public transport vehicles, residents and pedestrians.
10. | Plavi most | Direction towards Šumice | Allow public transport vehicles to continue moving forward from the right-turn lane.
11. | Vojislava Ilića | From Ustanička to Žička | Bus lane for public transport vehicles (both directions)– interrupted yellow line to Mis Irbijeve
12. | Kneza Miloša | Mostar interchange – Birčaninova | Bus lane for public transport vehicles in the morning peak hours towards the city (07:00-09:00), and in the afternoon peak hours towards Mostar (14:00-16:00).
13. | Karađorđeva, Savska | Faculty of Economy to Mostar | HoV lanes (from Mostar to Savski trg), it is necessary to consider prioritization in the design phase.
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 14
STREETS AND SECTIONS WITH PROPOSED CHANGES AND INTERVENTIONS
No. | Street | Section | Proposed operation mode intervention
14. | Highway | From the Zmaj interchange to the Lasta interchange | Promotion of HoV lanes (wherever possible) in both directions.
15. | Tabanovačka | Triše Kaclerovića to autokomanda | Change from one way traffic to both ways, for all vehicles.
16. | Bulevar Oslobođenja | Lepenička – roundabout | Road widening and introducing a bus lane for public transport vehicles from Lepenička street to the roundabout.
17. | Vojvode Stepe | From autokomanda to Save Maškovića | Changes in traffic and light signal operating modes.
18. | Crnotravska, Neznanog junaka | From Bahtijara Vagabzade to the roundabout | Three bus lanes with changeable signalling (stops with special extensions outside the main traffic flow)
19. | Save Maškovića | Bulevar oslobođenja – Vojvode Stepe | Road widening necessary, two lanes in the direction towards Vojvode Stepe.
20. | Radnička | Radnička Strugarska intrsection | Separate the left turn from Radnička into Strugarska.
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 15
STREETS AND SECTIONS WITH PROPOSED CHANGES AND INTERVENTIONS
No. | Street | Section | Proposed operation mode intervention
21. | Kirovljeva | Požeška to Visoka | Introducing a bus lane for public transport vehicles along the entire length of Kirovljeva street.
22. | Požeška – Kirovljeva intersection | Direction from Požeška towards Kirovljeva | Middle left-turn lane only for public transport.
23. | Požeška | From Kirovljeva to the tram overpass | Bus lane for public transport vehicles
24. | Blagoja Parovića | From Požeška to Kneza Višeslava | Stops in separate niches.
25. | Trgovačka | Intersection of Trgovačka towards Ace Joksimovića | Left turn from the middle lane for public transport vehicles. Enable a connection from this lane to the bus stop in Ace Joksimovića, by use of bus lane.
26. | Pilota Mihaila Petrovića | From Marička to Kneza Višeslava | (stops with special extensions outside the main traffic flow).
27. | Patrijarha Joanikija | From Pilota Mihaila Petrovića to the Vidikovac terminus | Stops in separate niches.
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 16
STREETS AND SECTIONS WITH PROPOSED CHANGES AND INTERVENTIONS
No. | Street | Section | Proposed operation mode intervention
28. | Jurija Gagarina | From Gandijeva to Ada Bridge | HoV lanes (both directions).
29. | Bulevar Mihajla Pupina, Bulevar Nikole Tesle | Intersection of Bulevar Mihajla Pupina and Bulevar Nikole Tesle | Traffic sign reading: “Do not block the intersection“.
30. | Bulevar Mihajla Pupina, Milentija Popovica | Intersection of Bulevar Mihajla Pupina and Milentija Popovića | Traffic sign reading: “Do not block the intersection“.
31. | Ada Bridge | Ada Bridge – Tošin bunar | Promotion of HoV lanes (wherever possible) in both directions.
25,3 km of new bus lines have been proposed and
the implementation of 43,5 km of HoV lanes
HoV lanes are used by public transport vehicles, taxi vehicles, vehicles carrying at least two people and emergency vehicles
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 17
PROPOSED EXPANSION OF BUS LANES IN BELGRADE

## Slide 18
SIMULATION OF PROPOSED SOLUTIONS
The simulation and description were performed using the model in the software package PTV VISUM
The existing version of the TMB is based on data from 2015, for this reason, the number of automobile journeys in the model was raised by 20%.

## Slide 19
SIMULATION OF PROPOSED SOLUTIONS

## Slide 20
DEFINITION OF BUS LANE OPERATION MODE
The analysis of the existing bus lanes retained the existing mode of functioning
Operating mode limits for bus lane use are 24 hours 7 days a week, An exception is made for bus lanes in Kneza Miloša Street where bus lane use follows changes in the alternating use of lanes
The bus lane system will function well if it is accompanied by sound monitoring and control measures. Control that bus lanes are not used by unauthorized vehicles will be performed in several ways:
  Control by authorities (police, communal police, inspections...)
  Fixed cameras set up to control bus lane use
  Traffic surveillance cameras on the territory of the city of Belgrade placed by the Ministry of Internal Affairs of the Republic of Serbia
  Public transport vehicle cameras
  "Hawkeye" system.
  For efficient control and monitoring, a system involving all relevant authorities must be established.

## Slide 21
THE DYNAMIC OF REALIZATION IN THE FIELD
No | Street | Section | 2021 | 2022 | 2023 | Note
1. | Kralja Milana, Terazije, Kolarčeva | From Slavija to Trg Republike |  |  |  | Realization in phases, design exists
2. | Resavska | from Bulevar kralja Aleksandra to Nemanjina |  |  |  | Prepare traffic signalization design
3. | Dečanska | From Bulevar Despota Stefana to Terazije tunnel |  |  |  | Prepare micro-simulation and traffic signalization design
4. | Brankova | Brankov most bus stop |  |  |  | Prepare civil design and traffic signalization design
5. | Ruzveltova, Mije Kovačevića | From Bulevar kralja Aleksandra to Omladinskog stadiona |  |  |  | Prepare traffic signalization design
6. | Bulevar kralja Aleksandra | From Kneza Miloša to Ruzveltova |  |  |  | Prepare traffic signalization design and correct light signalization design
 |  | From Cvetkova pijaca to Ustanička |  |  |  | After reconstruction is competed

## Slide 22
No | Street | Section | 2021 | 2022 | 2023 | Note
7. | Bulevar kralja Aleksandra | From Kneza Miloša to Ustanička |  |  |  | In accordance with the implementation of the project
8. | Cara Dušana, Dzordža Vašingtona, 27. marta, Kraljice Marije | Following completion of works – entire length |  |  |  | Following completion of reconstruction works, prepare traffic signalization design changes
9. | Dobračina | Entire lenth |  |  |  | Prepare traffic signalization design
10. | Plavi most | Towards Šumice |  |  |  | Prepare civil design of the intersection reconstruction and traffic signalization.
11. | Vojislava Ilića | From Ustanička to Žička |  |  |  | Prepare traffic signalization design
12. | Kneza Miloša | Mostar –Birčaninova intersection |  |  |  | The dynamic is dependent on the street reconstruction, Prepare traffic signalization design and the correction of the light signalization design.
THE DYNAMIC OF REALIZATION IN THE FIELD

## Slide 23
No | Street | Section | 2021 | 2022 | 2023 | Note
13. | Karađorđeva, Savska | Faculty of Economy to Mostar |  |  |  | Prepare traffic signalization design, amendment of the law, control and campaigns
14. | Highway | From the Zmaj interchange to the Lasta interchange |  |  |  | Traffic signalization design, amendment of the law, control, campaigns
15. | Tabanovačka | From Triše Kaclerovića to Autokomanda |  |  |  | Resolve property relations Complete civil design for the reconstruction and traffic signalization design
16. | Bulevar Oslobođenja | Lepenička– roundabout |  |  |  | Prepare civil design and traffic signalization design
17. | Vojvode Stepe | From autokomanda to Save Maškovića |  |  |  | It is necessary to complete a separate study and design.
18. | Crnotravska, Neznanog junaka | From Bahtijara Vagabzade to roundabout |  |  |  | In accordance with the implementation of the project
THE DYNAMIC OF REALIZATION IN THE FIELD

## Slide 24
No | Street | Section | 2021 | 2022 | 2023 | Note
19. | Save Maškovića | Bulevar oslobođenja – Vojvode Stepe |  |  |  | Implementation by Belgrade Land Development Agency. Check realization dynamics and solution
20. | Radnička | Radnička - Strugarska intersection |  |  |  | Prepare civil design and traffic signalization design
21. | Кirovljeva | Požeška to Visoka |  |  |  | Prepare traffic signalization design
22. | Požeška – Kirovljeva intersection | Direction from Požeška towards Kirovljeva |  |  |  | Prepare traffic signalization design
23. | Požeška | From Kirovljeva to the tram overpass |  |  |  | Prepare traffic signalization design
24. | Blagoja Parovića | From Požeška to Kneza Višeslava |  |  |  | Prepare civil design and traffic signalization design
25. | Trgovačka | Trgovačka intersection towards Ace Joksimovića |  |  |  | Prepare civil design and traffic signalization design
THE DYNAMIC OF REALIZATION IN THE FIELD

## Slide 25
No | Street | Section | 2021 | 2022 | 2023 | Note
26. | Pilota Mihaila Petrovića | From Marička to Kneza Višeslava |  |  |  | Prepare civil design and design of horizontal, vertical and light signalization
27. | Patrijarha Joanikija | From Pilota Mihaila Petrovića to Vidikovac Од Пилота Михаила Петровића до Vidikovac terminus |  |  |  | Prepare civil design and traffic signalization design
28. | Jurija Gagarina | From Gandijeva to Ada Bridge |  |  |  | Traffic signalization design, amendment of the law, control, campaigns
29. | Bulevar Mihajla Pupina, Milentija Popovića | Intersection of Mihajla Pupina and Milentija Popovića |  |  |  | Traffic signalization design and construction of pedestrian underpass
30. | Mihajla Pupina, Buleva Nikole Tesle | Intersection of Mihajla Pupina and Bulevar Nikole Tesle |  |  |  | Traffic signalization design
31. | Ada Bridge | Ada Bridge – Tošin Bunar |  |  |  | Traffic signalization design, amendment of the law, control, campaigns
THE DYNAMIC OF REALIZATION IN THE FIELD

## Slide 26
26
THANK YOU
FOR YOUR ATTENTION