## Slide 1: RESEARCH ON THE EFFECT OF DRIVING STYLE ON ENERGY EFFICIENCY OF ELECTRIC BUSES
Project Leader: Ivan Blagojević, Ph.D.
University of Belgrade Faculty of Mechanical Engineering

## Slide 2
Customer:
Secretariat for Public Transport of the City of Belgrade
Executant:
Faculty of Mechanical Engineering, University of Belgrade with
Innovation Center of the Faculty of Mechanical Engineering, University of Belgrade
Goal:
To investigate the effect the driving style has on energy efficiency of electric buses and the possibility of its improvement
Duration:
85 days
Phase 1: 50 days
Phase 2: 35 days
О пројекту
2 / 30
Project outline

## Slide 3
О пројекту
3 / 30
Tasks
Define the representative driving modes that take into account different values of acceleration, speed, deceleration, distance travelled and vehicle load
Define the method of measuring the energy recovery and consumption, as well as measuring acceleration and speed, with the description of measuring equipment to be used during testing
Test a single electric bus on a training ground according to acquired driving cycle with different values of acceleration and deceleration of the vehicle (low, medium and high) which will at that point be defined (with unloaded and loaded vehicle)
Acquire data on consumed and gained energy based on a representative number of measurements for each defined mode
After a statistical data evaluation, the proposition of recommended driving style to be done via optimal acceleration and deceleration band, which implies the maximum energy efficiency; Define driving styles for real conditions of exploitation to be used in Phase 2

## Slide 4
О пројекту
4 / 30
Tasks
Determination of criteria of efficiency control of the driver behavior based on driving style and expected effect on electric energy consumption by E-Bus based on the results from Phase 1
Based on determined criteria, testing of E-Bus on the training ground will take place, but in real conditions of exploitation on the EKO 1 route (Vukov spomenik – Belville). The driver will drive in different styles (economical , basic, aggressive) in order to verify the results from the training ground in real conditions
Training of drivers who drive the E-Bus with the purpose of using the vehicles more energy efficiently with the minimum electric energy consumption, but according to determined ecological driving style

## Slide 5
Electric bus HIGER KLQ6125GEV3
5 / 30
Test subject
2 asynchronous electric motors
SIEMENS IPV5135-4WS28

## Slide 6
Characteristic modes of electric bus testing on a training ground should cover different accelerations, driving with different constant speed, as well as different decelerations. Before defining testing modes, different values of speed in realistic driving conditions, with passengers on route EKO 1, were examined, where the speed of 40 km/h was rarely exceeded (only while crossing the Brankov bridge), based on what, during acceleration, speeds of 35 and 40 km/h may be assumed to be maximum achievable.
6 / 30
Driving modes

## Slide 7
Acceleration modes
Accelerator pedal position is the parameter according to which the driver affects the acceleration intensity. Therefore the testing of acceleration modes should cover constant accelerator pedal position, as well as variable accelerator pedal positions.
Mode | Vmax | 
Maximum acceleration (accelerator pedal position 100%) | 35 km/h | 40 km/h
Gradual change in accelerator pedal position (by driver’s feel) until the maximum value is reached |  | 
Gradual release of accelerator pedal (by driver’s feel) from the maximum position |  | 
Monitoring the curves of dependence of speed from time defined with the coefficient β = (0,7 - 2) |  | 
7 / 30
Driving modes
v = v0 + (vf–v0)·((t–t0)/(tf–to))β
v,v0,vf – current, initial and final speed [m/s]
t,t0,tf – current, initial and final acceleration time [s]

## Slide 8
Constant speed modes
Despite the constant speeds on route EKO 1 being rare, testing is done for different speed values ranging from 25 to 50 km/h, in order to determine constant speed at which the energy efficiency is highest.
Deceleration modes
Low, medium and high deceleration intensity are to be completed, with loaded and unloaded vehicle, in order to determine the amount of recuperated energy for different accelerator pedal positions, loading conditions and speeds before and during the braking process.
8 / 30
Driving modes

## Slide 9
Unloaded
7 examiners (total 490 kg)
9 / 30
Vehicle load
Loaded
50% max (as in SORT cycle)
Sand bags, 40 kg each
(total 3060 kg = 45 passengers, 68 kg each)
7 examiners (total 490 kg).

## Slide 10
Data acquisition unit – HBM QuantumX MX840A (qty. = 2)
Firewire HBM – cable for connecting and synchronization of acquisition units
Acceleration sensor – Monitran MTN/7100
GPS speed sensor Racelogic – Vbox
Laptop – Fujitsu Lifebook E series
Tablet – Samsung Galaxy Tab A
Software for data acquisition and analysis – CatmanAP V3.5.1
Router –Tenda N150 easy
Voltage converter (24V / 22V – sine-wave)
Inclinometer – WIT-motion SINIT232
10 / 30
Measuring equipment

## Slide 11
11 / 30
Measuring equipment

## Slide 12
Parameters monitored during testing:
Supercapacitor state of charge: АW_SOC_Battery [%]
Motor torque: ActualDriveMotorTorque [%]
accelerator pedal position: APPosition [%]
Brake pedal position: BrakePedalPosition [%]
Motor speed: DriveMotorSpeed [rpm]
Several parameters are monitored over analogue signals in such manner that the cables are connected on data acquisition unit from adequate supercapacitor connection points:
Supercapacitor current: I_uc [A]
Supercapacitor voltage: U_uc [V]
Invertor current: I_inv [A]
Longitudinal acceleration over separate sensor: Ubrzanje Monitran [g]
In order to check vehicle speed accuracy acquired over CAN, the speed sensor that bases its function on GPS and GLONAS signals is used.
Data acquisition frequency is 50 Hz, except for vehicle speed measured via sensor, where the sampling frequency is 5 Hz.
The most accurate signals for supercapacitor current and voltage are acquired from analogue signals.
12 / 30
Monitored parameters

## Slide 13
Values acquired during testing are saved in .BIN format in computer memory. Analysis the measured values is done with CatmanAP V3.5.1. Acquired data can be shown and analyzed with aforementioned software, whilst for project needs, the analysis was done in Microsoft Excel.
13 / 30
Result analysis methods
In order to determine the electric energy consumed and gained by recovery [kWh], it is a must, based on analogue signals for current and voltage, to calculate the electric motor power at any moment [kW], hence for each measured speed. Afterwards, to determine consumed/gained energy, the area below power curve is calculated.

## Slide 14
During the Phase 1 of the Project, there were three test days: November 15th, December 4th, and December 17th 2019.
Beforehand, trial test was enforced to determine the possibility of connecting the acquisition equipment with CAN and monitoring the adequate vehicle parameters, where the data acquisition in real conditions of exploitation on route EKO 1 takes place as well.
All three tests covered testing in real traffic conditions and training ground tests according to planned cycles.
The first test was done with unloaded bus (there were 6 test engineers and driver on board) , whilst the other two were done with payload defined in Section 6.2 (via sand bags placed uniformly.
Tests on training ground were done on sections “P”, “M”, “B” around GSP Novi Beograd Depot near Belville, because the traffic conditions were appropriate.
Also, the fast-charge charger availability was crucial in order to repeat the modes with the same state of charge of supercapacitor.
The Second Phase tests implied the monitoring of characteristic parameters in real conditions of exploitation on route EKO 1, in the mode recommended by the project and the mode that can be considered non-economical, but considered realistic by the GSP drivers.
14 / 30
Results analysis

## Slide 15
15 / 30
Results analysis
Vconst =
30 km/h
Vconst =
35 km/h
Vconst =
40 km/h
Vconst =
50 km/h

## Slide 16
Acceleration mode | Section
Maximum acceleration | B
 | P
 | М
 | B
 | P
 | М
Gradual increase in accelerator until maximum | B
 | P
 | М
Gradual decrease in accelerator pedal position until determined percentage | B
 | P
 | М
β = 0,7 | B
 | P
 | М
β = 0,85 | B
 | P
 | М
β = 1,4 | B
 | P
 | М
16 / 30
Training ground tests

## Slide 17
Cycle number/ section | Energy consumed until speed of 35 km/h [kWh] | Energy consumed until speed of 40 km/h [kWh] | Energy gained during braking [kWh] | Supercapacitor voltage in the beginning (UUCp) and in the end (UUCk) of cycle [V] | Parameter of characteristics of acceleration [-]
2/M | Epot35 = 0.298 | Epot40 = 0.379 | Ereg = 0.113 | UUCp, UUCk = 569, 548 | β ≈ 0.7
3/B | Epot35 = 0.283 | Epot40 = 0.382 | Ereg = 0.101 | UUCp, UUCk = 561, 540 | β ≈ 0.7
5/M | Epot35 = 0.311 | Epot40 = 0.391 | Ereg = 0.109 | UUCp, UUCk = 570, 551 | β ≈ 0.85
6/B | Epot35 = 0.293 | Epot40 = 0.395 | Ereg = 0.125 | UUCp, UUCk = 563, 547 | β ≈ 0.85
8/M | Epot35 = 0.313 | Epot40 = 0.399 | Ereg = 0.095 | UUCp, UUCk = 554, 533 | β ≈ 0.85
9/B | Epot35 = 0.309 | Epot40 = 0.389 | Ereg = 0.094 | UUCp, UUCk = 546, 526 | β ≈ 0.85
10/P | Epot35 = 0.306 | Epot40 = 0.395 | Ereg = 0.114 | UUCp, UUCk = 575, 560 | β ≈ 0.85
11/M | Epot35 = 0.306 | Epot40 = 0.402 | Ereg = 0.116 | UUCp, UUCk = 571, 554 | β ≈ 0.85
12/B | Epot35 = 0.299 | Epot40 = 0.387 | Ereg = 0.105 | UUCp, UUCk = 565, 544 | β ≈ 0.85
13/P | Epot35 = 0.310 | Epot40 = 0.410 | Ereg = 0.074 | UUCp, UUCk = 576, 560 | -
14/M | Epot35 = 0.299 | Epot40 = 0.386 | Ereg = 0.121 | UUCp, UUCk = 573, 553 | β ≈ 1.4
15/B | Epot35 = 0.280 | Epot40 = 0.374 | Ereg = 0.113 | UUCp, UUCk = 567, 546 | β ≈ 1.4
16/P | Epot35 = 0.297 | Epot40 = 0.384 | Ereg = 0.125 | UUCp, UUCk = 560, 540 | β ≈ 1.4
19/P | Epot35 = 0.302 | Epot40 = 0.388 | Ereg = 0.113 | UUCp, UUCk = 576, 557 | β ≈ 1.4
21/B | Epot35 = 0.282 | Epot40 = 0.363 | Ereg = 0.084 | UUCp, UUCk = 567, 547 | β ≈ 1.4
23/M | Epot35 = 0.301 | Epot39 = 0.414 | Ereg = 0.046 | UUCp, UUCk = 558, 551 | -
24/B | Epot35 = 0.294 | Epot40 = 0.399 | Ereg = 0.117 | UUCp, UUCk = 551, 532 | -
25/P | Epot35 = 0.291 | Epot40 = 0.376 | Ereg = 0.094 | UUCp, UUCk = 545, 527 | β ≈ 0.7
26/M | Epot35 = 0.290 | Epot40 = 0.381 | Ereg = 0.045 | UUCp, UUCk = 542, 523 | β ≈ 0.7
27/B | Epot35 = 0.270 | Epot40 = 0.367 | Ereg = 0.139 | UUCp, UUCk = 535, 516 | β ≈ 0.7
17 / 30
Training ground tests

## Slide 18
18 / 30
Results analysis
13/P: Epot35 = 0.310 kWh; Epot40 = 0.410 kWh; Ereg = 0.074 kWh; 25/P: Epot35 = 0.291 kWh; Epot40 = 0.376 kWh; Ereg = 0.094 kWh; β ≈ 0.7

## Slide 19
19 / 30
Results analysis
8/M: Epot35 = 0.313 kWh; Epot40 = 0.399 kWh; Ereg = 0.095 kWh; β ≈ 0.85 26/M: Epot35 = 0.290 kWh; Epot40 = 0.381 kWh; Ereg = 0.045 kWh; β ≈ 0.7

## Slide 20
20 / 30
Results analysis
9/B: Epot35 = 0.309 kWh; Epot40 = 0.389 kWh; Ereg = 0.094 kWh; β ≈ 0.85 27/B: Epot35 = 0.270 kWh; Epot40 = 0.367 kWh; Ereg = 0.139 kWh; β ≈ 0.7

## Slide 21
In constant speed driving mode, the optimal value is around 35 km/h.
In acceleration modes, in which the accelerator pedal position does not have a continual rate (positive or negative), also where accelerator pedal position does not gradually increase or decrease, but its position oscillates, the energy consumed is visibly higher. This can be explained with the effect of rotating masses of drivetrain and transmission, and also the inertia of the whole vehicle.
The differences in consumed energy for different cycles can be described with almost the same value of the parameter on the same section. In fact, in case the driver accomplishes requested acceleration by continual position change of accelerator pedal, the consumed energy would also decrease. Nevertheless, if the requested speed is reached by alternating increase and decrease of accelerator pedal position, energy consumed is higher.
In case the driver keeps accelerator pedal position at maximum, there are no oscillations, so that seemingly energetically inefficient mode of maximum acceleration gives the best outcome.
In any case, that effect would be even higher if the maximum position of accelerator pedal is reached by its continual, and not abrupt alteration.
21 / 30
Results and recommendations

## Slide 22
Large differences in recovered energy are a result of a large specter of applied means of braking in cycles: from very intense braking (8/М), over controlled extended (27/B), to abrupt braking (26/М). Braking torque of electric motor or generator, that ensures energy recovery, increases with the change in position (%) of brake pedal until the maximum value is reached, so that the intense braking (greater deflection of brake pedal) ensures only the shorter stopping time, but not the greater energy recovery. In other words, extended braking with smaller deflection of brake pedal ensures greater energy recovery, and in turn more efficient use of regenerative braking.
Real evidence for that is already mentioned cycle 27/B. Brake pedal, if the traffic allows, should be kept in the interval from 0 to 9°, which means 0 to 28% of maximum position, which would permit only the regenerative braking in the range up to maximum brake torque of electric motor or generator.
Energy recovery by vehicle inertia without braking is nonetheless more efficient if the traffic conditions allow it.
22 / 30
Results and recommendations

## Slide 23
Based on recommendations, the ideal cycle between two stops consists of continual acceleration mode and deceleration by inertia and/or braking in recommended limits. For small amount of acceleration distance travelled is 500 m and 350 m for maximum speed of 50 km/h and 40 km/h, respectively. This cycle is different from recommended cycle for the bus with an internal combustion engine, for the same distance travelled.
23 / 30
Results and recommendations
Internal combustion engine bus
Electric bus
t

## Slide 24
In order to perceive the effect of driving style, it is necessary to construct criteria needed to perceive the effect of driving style:
Total consumed energy per route, that has to be observed with respect to duration of travel. The outliers, both positive and negative, have to be observed with the respect to the number of passengers on board during travel, which can be done by observing the video made during the travel in focus.
Total recovered energy per route, that has to be observed with the respect to duration of travel
The ratio of recovered and consumed energy as a relative indicator excluding the duration of travel
24 / 30
Results and recommendations

## Slide 25
The change of speed throughout the time, observed in a diagram of speed versus time for each of the acceleration modes
Brake pedal position, observed in a diagram of the brake pedal position versus time for each of the acceleration modes
The share of time spent coasting versus total time of travel, meaning the ratio of time where accelerator pedal position and brake pedal position have the value of 0% while the vehicle is in motion (speed greater than zero) and the total time spent in motion (speed greater than zero)
25 / 30
Results and recommendations

## Slide 26
The effect of recommendations for energy efficient driving of electric buses on route EKO 1 is confirmed in the Phase 2 of the Project by testing in real conditions of exploitation.
First two cycles (from Vukov Spomenik to Belville and back), the driver drove according to recommendations and under supervision.
Next two cycles (from Vukov Spomenik to Belville and back), the driver drove “aggressively” based on real (everyday) experience.
26 / 30
Results and recommendations
Vukov Spomenik to Belville | E_consumed total [kWh] | E_recovered total [kWh] | E_recovered [%] | Time [min]
Economically | 9.559 | 2.789 | 29.182 | 30.377
Aggressively | 11.766 | 2.890 | 24.566 | 27.511
Difference | 23% |  |  | 
Belville To Vukov Spomenik | E_consumed total [kWh] | Е_recovered total [kWh] | E_recovered [%] | Time [min]
Economically | 12.944 | 2.258 | 17.443 | 34.331
Aggressively | 16.907 | 2.453 | 14.509 | 35.804
Difference | 30% |  |  | 

## Slide 27
27 / 30
Results and recommendations
Cycle between two stops lasting 52 s while driving economically in real conditions of exploitation
Cycle between two stops lasting 52 s while driving aggressively in real conditions of exploitation
Two consecutive cycles between stops lasting 33 s each when driving economically in real conditions of exploitation

## Slide 28
28 / 30
Results and recommendations
Vukov Spomenik to Belville | Mean value of speed [km/h] | Share of braking in total amount of time spent in motion [%] | Mean value of brake pedal position [%] | Share of coasting in total amount of time spent in motion [%] | Share of coasting in total distance of travel [%] | Total duration of motion [min] | Total duration of travel [min]
Economically | 20.67 | 11.43 | 6.63 | 27.38 | 49.67 | 20.17 | 30.377
Aggressively | 24.17 | 17.43 | 6.94 | 12.43 | 21.54 | 17.37 | 27.511
Belville to Vukov Spomenik | Mean value of speed [km/h] | Share of braking in total amount of time spent in motion [%] | Mean value of brake pedal position [%] | Share of coasting in total amount of time spent in motion [%] | Share of coasting in total distance of travel [%] | Total duration of motion [min] | Total duration of travel [min]
Economically | 19.96 | 6.30 | 5.48 | 32.23 | 50.04 | 24.87 | 34.33
Aggressively | 24.41 | 13.48 | 6.97 | 9.28 | 17.90 | 20.37 | 35.80

## Slide 29
29 / 30
Instead of conclusion
All scheduled activities were completed
Matters for future research:
Driving style and the effects of training of each driver are to be quantified and monitored constantly
Recommendations for energy efficient driving and outcome indicator for the driver in real time
Recommendation for specific sections between two stops (bus-stops, traffic lights), taking into account the section length and the travel duration based on current traffic conditions
It is necessary to take into account the energy consumed by auxiliary consumers, especially cooling and heating systems, because there a considerable savings can occur.

## Slide 30: Thank You for Your attention!
30 / 30